## Slide 1: CrashTwin
PROGRESS REPORT · 30 OCTOBER 2026
A CARLA digital twin that teaches crash anticipation, tested on real dashcam video
Adarsh L · CAVE Labs, PES University
2,576
CARLA clips generated
26
models trained
6
experiments, E1–E6
2 of 4
days used for all compute
Notes: Status after the 4-day sprint: every compute step is finished (generation, tracking, 26 training runs, E5, E6). This deck covers the problem, how CrashTwin works, the data, the results of E1–E6, the problems we hit, progress, what is left, and how the project moves to the new GPU machine.

## Slide 2: Real crash data is scarce and camera-only
Problem statement: crash warning needs many crashes, every sensor and consistent labels; no dataset has all three
1,500
real crash clips in CCD
the largest public dashcam crash set; Nexar adds 1,500 videos. Internet video, camera only, labelled by people
Very few
real crash recordings with radar or LiDAR
multi-sensor driving datasets hold almost no crashes; Accid3nD records crashes from roadside cameras, not from a car
Unlimited
crashes a simulator can make
with every sensor and exact labels, but synthetic crash data had not been tested on real dashcam crashes
CrashTwin asks: can a validated CARLA twin teach a model to warn before real crashes?
Notes: Real crash videos are few, camera-only and labelled inconsistently. Simulators can make unlimited crashes with every sensor, but nobody had checked whether synthetic crashes help on real dashcam crashes. That gap is CrashTwin's question.

## Slide 3: Four research questions
Each question maps to one experiment; status as of today
RQ1 · Sim-to-real · E1–E3
Can a model trained on CARLA anticipate real crashes, alone or added to real data?
Answered: yes on Nexar, no on CCD
RQ2 · Sensor fusion · E4
How much do radar, LiDAR and depth add to the camera?
Answered in simulation: +0.09 to +0.13 AP in the unseen town
RQ3 · Twin fidelity · E5
Does CARLA's traffic behave like real traffic?
Answered: CARLA traffic is slower and calmer
RQ4 · Conditions · E6
Do night and rain hurt real and simulated crashes alike?
Not yet clear: the night and rain groups are small
Notes: RQ1 is the main question. RQ2 to RQ4 explain where the twin helps and where it does not.

## Slide 4: Headline results
Mean of 2 seeds per configuration; details on the results slides
0.63
Nexar mAP from CARLA only
as good as 10–25 % of the real training data (chance ≈ 0.5)
0.25
CCD AP from CARLA only
below the 0.31 chance level: the twin does not transfer to CCD
+0.03
Nexar private mAP from adding CARLA to all real data
0.681 → 0.714; on CCD it costs 0.867 → 0.844
0.84 → 0.97
Unseen-town AP with radar + LiDAR + depth
in simulation, so an upper bound for real sensors
107 / 133
CCD source videos in both official train and test
we evaluate on a source-grouped split instead
Notes: Main message: the twin helps on Nexar, especially when real data is scarce, but not on CCD. Range sensors help a lot inside the simulator. CCD's official split leaks source videos.

## Slide 5: How CrashTwin works
One pipeline for simulated and real video; no simulator ground truth ever reaches a real-video model
1. CARLA generator
13 scenario families, 6 towns, 8 weathers, 3 traffic densities
2. Measured labels
crash, near-miss or normal from collisions and TTC; 20+ checks per clip
3. YOLO11s + ByteTrack
the same frozen detector and tracker for CARLA and real video
4. 83 camera features
box growth, image TTC, ego motion; + 8 sensor features in CARLA
5. Causal GRU
a crash probability for every frame, before the event
6. Evaluation
Nexar and CCD: AP, mAP, warning time, false alarms
Real video (CCD, Nexar) enters at step 3, so CARLA and real clips get identical inputs.
Notes: CARLA clips and real clips go through the same detector, tracker and features. The model never sees simulator ground truth for real video, so E1 to E3 compare training data only.

## Slide 6: 13 scenario families, controlled conditions
Every clip: 10 s at 10 Hz, event at frame 60–90 after a ≥ 3 s warm-up; the scenario's intent never sets the label
Crash · C1–C5
Rear-end
Cut-in
Junction
Pedestrian or cyclist crossing
Single vehicle into a pole
Near-miss · N1–N4
Rear-end avoided
Cut-in avoided
Junction conflict
Pedestrian or cyclist conflict
Normal · R1–R4
Car following
Junction approach
Lane change
Pedestrian or cyclist nearby
Towns
Town01, 02, 03, 04, 10HD for training; Town05 held out for testing
Weather and light
8 conditions: clear noon, sunset, night, cloudy, wet, rain night, hard rain, fog
Sensors
RGB 1280×720, depth, 32-channel LiDAR, radar, IMU, GNSS, collision; all synchronised by frame
3 traffic densities. Actors are placed in advance (no pop-in); triggers are timed in closed loop.
Notes: Near-miss families add a seeded emergency brake for the ego car. Normal families give the negatives. Town05 never appears in training or validation.

## Slide 7: Labels are measured, never assumed
Outcome comes from the collision sensor and a predicted-overlap time-to-collision (TTC), then 20+ automatic checks
Crash
any collision of the ego car
Near-miss
no collision; the same actor comes within 1.5 m and ≤ 1.5 s TTC
Normal
no collision and minimum TTC above 3 s
Invalid
anything in between: kept on disk, never trained on
Checks: synchronisation, files, labels, physics, provenance → PASS / WARN / FAIL. A clip is usable when nothing FAILs.
0
synchronisation failures in the pilot (243 clips)
0.04–0.11 m
median sensor-to-truth gap error (depth, LiDAR, radar)
24
unit tests, all passing
Notes: The predicted-overlap TTC replaced a gap divided by closing speed rule that wrongly flagged oncoming and passing traffic. Sensor errors are agreement with CARLA ground truth, not proof of real-world realism.

## Slide 8: Data: one twin, three real datasets
Splits are by scenario slot (CARLA) or by source video (CCD), never by frame
Dataset | What it is | Size | Split | Used in
CrashTwin (CARLA) | ego dashcam + 7 sensors, measured labels | 2,576 clips; 1,877 usable (852 crash, 276 near-miss, 749 normal) | train 1,031 · val 220 · test 245 · Town05 381 | E1, E3, E4, E6
CCD | YouTube dashcam clips, 5 s at 10 fps | 1,500 crash + 3,000 normal | source-grouped 80/10/10 (test 437 videos, 31 % crashes); official split also reported | E2, E3, E6
Nexar | dashcam, ~40 s; collisions and near-misses | 1,500 training videos; test 667 public + 677 private | official partitions; 15 % of training for validation | E2, E3, E6
Accid3nD | roadside highway cameras with 3D labels | 10,454 car-following samples | not used for training | E5
Pilot clips are never used. Licensed data (Nexar, Accid3nD) and features made from it stay private.
Notes: Usable CARLA clip = no FAIL and a valid measured outcome. Positives are crash or near-miss. The full run stopped at the 40 GB storage cap after 3,040 of 3,300 slots; the 260 unrun slots are Town10HD normal driving.

## Slide 9: CCD's official split leaks source videos
Clips cut from the same YouTube video sit on both sides of the official train/test split
107 of 133
source videos appear in both official train and test
1 of 300
official test crashes comes from a source unseen in training
So we train and test on a source-grouped split (80/10/10) and report the official split only for comparison.
Chart: Real-only model (E2): CCD AP by split
| 10 % | 25 % | 50 % | 100 %
Source-grouped split (ours) | 0.678 | 0.745 | 0.846 | 0.867
Official split | 0.709 | 0.779 | 0.883 | 0.924
Notes: The official split gives higher AP at every real-data fraction (+0.03 to +0.06), as expected from shared source videos. Our primary CCD number is always the grouped split.

## Slide 10: Nexar: CARLA alone ≈ 10–25 % of real data
Nexar official test sets (mean of public and private mAP); chance ≈ 0.5
Chart: Nexar mAP vs real training data
| 10 % | 25 % | 50 % | 100 %
Real only (E2) | 0.556 | 0.608 | 0.665 | 0.692
CARLA + real (E3) | 0.602 | 0.629 | 0.659 | 0.711
CARLA only (E1, no real data) | 0.63 | 0.63 | 0.63 | 0.63
0.63
CARLA only
above chance, between the 10 % and 25 % real-data models
+0.05
CARLA added to 10 % real
0.556 → 0.602: the twin helps most when real data is scarce
0.714
best private-test mAP
CARLA + all real data (real only: 0.681)
2 seeds; differences under 0.03 are within seed noise.
Notes: Nexar public / private mAP. CARLA only: 0.621 / 0.638. Real only at 10, 25, 50, 100 %: public 0.586, 0.640, 0.664, 0.703; private 0.526, 0.576, 0.666, 0.681. CARLA + real: public 0.619, 0.652, 0.640, 0.707; private 0.585, 0.606, 0.678, 0.714.

## Slide 11: CCD: the twin does not transfer
CCD source-grouped test: 437 videos, 31 % crashes (chance AP ≈ 0.31)
Chart: CCD AP vs real training data
| 10 % | 25 % | 50 % | 100 %
Real only (E2) | 0.678 | 0.745 | 0.846 | 0.867
CARLA + real (E3) | 0.535 | 0.633 | 0.797 | 0.844
CARLA only (E1, no real data) | 0.249 | 0.249 | 0.249 | 0.249
0.25
CARLA only
below the 0.31 chance level: it ranks crashes worse than guessing
−0.14
adding CARLA to 10 % real
0.678 → 0.535; the cost shrinks as real data grows (−0.02 at 100 %)
Why?
not tested yet
5 s clips, other camera heights, many crashes between other cars, not the dashcam car
Notes: CCD is where the twin fails. Checking CCD crashes that involve the dashcam car separately from crashes between other vehicles is the first analysis to run next.

## Slide 12: Range sensors help most in the unseen town
E4, CARLA test sets: camera features alone vs camera + sensor features
Chart: CARLA test AP (CCD protocol)
| camera | + radar | + LiDAR | + depth | + all
Familiar towns | 0.912 | 0.959 | 0.955 | 0.959 | 0.966
Town05 (held out) | 0.837 | 0.93 | 0.926 | 0.94 | 0.971
+0.09 to +0.10
AP from any one range sensor
in Town05, where the camera alone generalises worst
0.971
all sensors, held-out town
camera alone: 0.837
Upper bound
simulated sensors
real radar and LiDAR noise will reduce these gains
Notes: Sensor features: radar range, closing speed and TTC; LiDAR and depth gap ahead; ego speed and IMU. Same GRU, same splits; only the input features change.

## Slide 13: CARLA traffic is slower and calmer
E5: car-following in real highway traffic (Accid3nD) vs CARLA's Town04 highway, medians
Speed
18.8 m/s
real highway
8.1 m/s
CARLA highway
Gap to the car ahead
27.9 m
real highway
18.9 m
CARLA highway
Time headway
1.58 s
real highway
2.15 s
CARLA highway
TTC when closing in
2.1 s
real highway
6.2 s
CARLA highway
10,454 real vs 437 CARLA samples at 1 Hz; speed, gap and headway differ at KS p < 10⁻³⁰, TTC at p < 10⁻⁸. The crash-level comparison was dropped: 0 of 3 automatic Accid3nD crash candidates were real crashes.
Notes: CARLA's Traffic Manager drives slower and keeps longer headways, so CARLA normal driving is calmer than reality. Only 30 CARLA samples were closing in, so the TTC comparison is weak.

## Slide 14: Night and rain: no clear effect yet
E6: video-level AP on Nexar public test by condition (CCD normal clips carry no condition labels)
Condition | Videos | CARLA only | Real only | CARLA + real
Normal light | 608 | 0.61 | 0.63 | 0.64
Dark | 21 | 0.37 | 0.59 | 0.54
Clear | 458 | 0.66 | 0.68 | 0.68
Rain | 32 | 0.51 | 0.56 | 0.53
Urban | 315 | 0.63 | 0.65 | 0.63
Highway | 183 | 0.86 | 0.69 | 0.73
Small groups
only 21 dark and 32 rain videos: confidence intervals overlap, and Nexar private reverses the rain result
Highway transfers
CARLA-only training scores 0.86 on highway videos vs 0.69 for real-only: the clearest sim-to-real win
In CARLA
night is not harder; wet noon is the weakest condition in Town05 (20 clips)
Notes: Hypotheses fixed before looking: AP night < day and AP rain < clear. Neither is clearly supported with these group sizes.

## Slide 15: Problems we hit, and the fixes
All logged in docs/INCIDENTS.md; no data was lost, overwritten or deleted
CARLA crashed in Town03_Opt
its Traffic Manager file is broken in 0.9.15: we use Town03
First TTC rule flagged passing cars as near-misses
replaced by predicted-overlap TTC and a same-actor rule before any data was made
CARLA's Python client crashed ~10 times
a supervisor restarts it; every attempt is logged first, so none is lost or replayed
A restart resumed the wrong run folder
lost ~15 min; the run folder is now fixed up front, early results archived, not deleted
Accid3nD crash detection: 0 of 3 were crashes
E5 switched from crash kinematics to traffic kinematics
CCD's official split leaks source videos
source-grouped split for all CCD results
Full run hit the 40 GB storage cap
stopped at slot 3,040 of 3,300 as designed; 260 Town10HD normal slots unrun
Training exits with an error after saving
Windows/CUDA teardown; results were saved, and job chains continue
Notes: The storage stop and the post-save training errors were expected behaviour. The wrong-folder resume was the only incident that cost time.

## Slide 16: Progress: all compute done in 2 of 4 days
What was built and run, in order
1
29 Oct, morning
Setup and data
environment, CCD, Nexar and Accid3nD downloaded (93 GB), full project plan
2
29 Oct, afternoon
Generator v2 and pilot
design docs, generator, validator, 24 tests; pilot: 243 clips, 0 sync failures
3
29 Oct, evening
Full run and real models
3,300-slot generation started; real video tracked; E2 trained
4
30 Oct, overnight
CARLA models
2,576 clips tracked and cached; E1, E3, E4 trained (26 runs total)
5
30 Oct, morning
Analysis and hand-over
E5, E6, figures, paper results, portable code, transfer kit, this deck
✓ Generator
✓ Pilot
✓ Full CARLA data
✓ 26 models
✓ E1–E6
✓ Paper results
✓ New-machine kit
Notes: The four-day plan's compute finished in two days. The remaining days can go to more seeds, the CCD analysis and writing.

## Slide 17: What's left
Five things only you can do, then optional work that would strengthen the paper
Needs you
Nexar licence review with the supervisor (decision D6)
Delete the exposed Hugging Face token 'carla-pc'; make a new one
Push the committed code to a private GitHub repo as adarshlaxman
Check the citations marked [verify] in the paper
Read paper/draft.md and say what to change
Recommended next (optional)
3 more seeds (5 total)
~30 min of training; makes small differences trustworthy
Why CCD fails
split CCD crashes into dashcam-car vs other-car crashes
Realistic CARLA traffic
faster, closer following; regenerate some normal clips (E5 gap)
Finish the 260 unrun slots
~1 h; needs the storage cap raised from 40 to 45 GB
Submit
IEEE ITSC / IV workshop or arXiv after the licence review
Notes: Recommended order: more seeds first (cheap), then the CCD analysis, then traffic realism.

## Slide 18: Moving to the new machine
Code goes to GitHub; data and results go by drive (full guide: docs/SETUP_NEW_MACHINE.md)
< 1 min
1 · Code to GitHub
Code is committed. Create an empty private repo 'crashtwin', then git push and sign in as adarshlaxman.
1–30 min
2 · Data by drive
0.32 GB results zip is enough to continue. Everything (~140 GB) via external drive with transfer.py.
~30 min
3 · Set up and resume
Clone, run setup_env, unzip results, then check_env and pipeline.py status (26/26 runs).
Why not put the data on GitHub?
GitHub refuses files over 100 MB (our Accid3nD zips are ~9 GB each) and expects repos under a few GB; we have ~140 GB. The datasets also carry licence conditions (Nexar: under supervisor review; Accid3nD: CC BY-NC-SA), so we never re-host them. Keep the repo private until the licence review.
Notes: Over the internet, 140 GB takes about 6 hours at 50 Mbps upload; an external USB 3 drive takes 15 to 30 minutes each way.

## Slide 19: Where CrashTwin stands
Three things to remember
1
A validated twin that helps on Nexar
CARLA alone reaches 0.63 mAP; with all real data it gives the best private score (0.714)
2
But not on CCD, yet
CARLA-only AP 0.25 is below chance; understanding why is the next research step
3
Sensors and realism point the way
range sensors lift held-out-town AP to 0.97; CARLA traffic must get faster and closer
Next: more seeds → CCD analysis → realistic traffic → submit
Notes: Questions welcome. Results tables: outputs/results/RESULTS.md and paper/draft.md section 7.